## Slide 1
REHEATING FURNACE ZONE SETPOINT
Corrected Model · Real Schedules · Interactive Prototype
Hazira RHF#1 · Nov 2025–Jan 2026 · 19,406 Slabs · 4 Real Schedules Compared
CORRECTION ADDRESSED IN THIS DECK
"Zone 8 temperature appears lower than FCE dropout — is this wrong?"
No. Z8 is an EQUALISING zone, not a heating zone. The slab arrives at Z8 already at ~1,310°C from soaking zones (Z3/Z4). Z8 homogenises top-bottom temperature differences before discharge. The FCE pyrometer reads slab surface temperature at exit — driven by stored soaking heat, moderated by Z8's cooler atmosphere. This is physically correct.
Z1
Preheat
Offset: +6°C
Z2
Preheat
Offset: +3°C
Z3
SOAKING
Offset: +77°C
Z4
SOAKING
Offset: +71°C
Z5
Heating
Offset: +18°C
Z6
Heating
Offset: +14°C
Z7
Heating
Offset: +17°C
Z8
Equalise
Offset: +8°C
← Slab travels this direction through furnace →
FCE Dropout = Slab surface temp at exit. Driven by Z3/Z4 soaking heat, NOT Z8 atmosphere.
+77°C
Z3 Soaking Offset
+71°C
Z4 Soaking Offset
+8°C
Z8 Equalising Offset
~1,238°C
FCE Dropout Mean

## Slide 2
CORRECT ZONE TEMPERATURE MODEL — Offset Above Recipe Target
Derived from 19,406 real slabs
Zone Setpoint = Recipe Target + Zone-Specific Offset
Z1
+6°C → 1237°C
Preheat entry. Cold slab warm-up. Modest offset — slab not yet in thermal contact.
Z2
+3°C → 1234°C
Continues preheat. Small offset — transitioning to higher-T zones.
Z3
+77°C → 1308°C
PRIMARY SOAKING ZONE. Furnace atmosphere hottest here — drives core temperature.
Z4
+71°C → 1301°C
Secondary soaking. Maintains slab core at target. Still far above exit temp.
Z5
+18°C → 1248°C
Heating transition. Slab core near target. Reduced zone–slab ΔT.
Z6
+14°C → 1245°C
Continues heating. Slab and atmosphere converge.
Z7
+17°C → 1247°C
Final heating. Atm slightly above slab for last push.
Z8
+8°C → 1237°C
EQUALISING ZONE. Homogenises top-bottom ΔT. Atm ≈ slab surface. Can be ≤ FCE dropout.
Zone Temperature Profile vs FCE Dropout (Recipe = 1230°C example)
FCE Dropout ~1238°C
Recipe 1230°C
Z1
1236
Z2
1233
Z3
1307
Z4
1301
Z5
1248
Z6
1244
Z7
1247
Z8
1238
1200
1250
1300
1350
1400
Z8 (equalising) at 1,237.6°C is BELOW FCE dropout of 1,238°C — correct because slab surface temp retains heat from Z3/Z4 soaking while Z8 atmosphere is cooler than soaking zones. This is expected furnace physics.

## Slide 3
THREE MODELS — Logic, Formula & Zone Setpoint Derivation
MODEL 1 — MAXIMUM SETPOINT
SP = max(R₁, R₂, ..., Rₙ)
HOW IT WORKS:
Finds the HIGHEST recipe temp among all slabs in furnace
Sets all 8 zones to: SP + zone_offset (Z3: +77°C, Z4: +71°C, Z8: +8°C...)
Every slab guaranteed to reach its recipe — even the hottest grade
Simple: one number, no weighting, no computation risk
WHEN TO USE
New grades under trial · Quality-critical campaigns · FCE dropout history shows underheating · Spread >18°C
TRADE-OFF
Overheats low-T grades by the full spread amount (e.g. +20°C for 1220°C grades when max=1240°C)
MODEL 2 — MASS-WEIGHTED AVERAGE
SP = Σ(Wᵢ × Rᵢ) / ΣWᵢ + 5°C buffer
HOW IT WORKS:
Weights each slab's recipe by its mass (heavier slab = more thermal inertia = more weight)
Adds 5°C safety buffer above raw weighted average
If any grade recipe > wtavg+10°C → apply zone-level override for that grade
Zone setpoints = SP + zone_offset (same offsets, lower base SP)
WHEN TO USE
Stable production · Known grade behaviour · Spread 5–15°C · Energy-saving campaigns
TRADE-OFF
High-recipe grades at tail risk if they are few and lightweight; mitigated by buffer + override rule
MODEL 3 — RESIDENCE-TIME WEIGHTED
SP = Σ(RTᵢ × Rᵢ) / ΣRTᵢ + 5°C buffer
HOW IT WORKS:
Weights by residence time: slabs staying longer need more heating → recipe gets more weight
Physically meaningful: long-RT slabs were likely cold-charged and need proportionally more heat
Matches thermal demand better when RT varies widely (>40 min spread across grades)
At Hazira, RT spread is moderate — M3 ≈ M2 most hours, but diverges for cold-charge schedules
WHEN TO USE
Mixed cold-charging/hot-charging · Wide RT variance (>40 min) · Schedules 20260014
TRADE-OFF
Requires real-time residence time data; slightly more complex than M2 for similar result on uniform-charge schedules

## Slide 4
REAL SCHEDULE COMPARISON — 4 Production Schedules vs 3 Models
Schedule
FCE
Actual
M1 Max
Setpt
M2 WtAvg
+5°C
M3 RTWt
+5°C
% Below
Recipe
Gas Save
M1→M2
Rec.
Sched 20260019
109sl · 16gr
1243.2°C
1240.2°C
1233.3°C
1232.1°C
14%
~635 NM3
M1
14% slabs below recipe → M1 for zero risk
Sched 20260015
90sl · 20gr
1245.1°C
1240.2°C
1231.1°C
1230.3°C
0%
~753 NM3
M2
Zero underheating, +19°C over-firing → M2 saves fuel
Sched 20260014
96sl · 18gr
1231.8°C
1240.2°C
1232.1°C
1231.5°C
21%
~700 NM3
M3
21% below recipe, wide RT spread → M3 RT-weighted
Sched 20260018
101sl · 16gr
1250.0°C
1240.2°C
1236.6°C
1235.5°C
0%
~459 NM3
M2
Zero underheating, heavy high-T grades → M2 balanced
% Below Recipe = slabs whose FCE dropout fell below their recipe target (quality risk indicator) · Gas Save = estimated NM3/HR saving by using M2 vs M1 (at 53.4 NM3 per °C sensitivity)
Setpoint Comparison Across Schedules
Chart: 
| S19 | S15 | S14 | S18
M1 Max | 1240.2 | 1240.2 | 1240.2 | 1240.2
M2 WtAvg+5°C | 1233.3 | 1231.1 | 1232.1 | 1236.6
M3 RTWt+5°C | 1232.1 | 1230.3 | 1231.5 | 1235.5
Actual FCE | 1243.2 | 1245.1 | 1231.8 | 1250

## Slide 5
ZONE SETPOINT PROFILES — All Models · Schedule 20260018 (Recommended M2)
Chart: Zone Setpoint (°C) by Zone — Schedule 20260018
| Z1 | Z2 | Z3 | Z4 | Z5 | Z6 | Z7 | Z8
M1 Max Setpoint (1240.2°C) | 1246.1 | 1243.2 | 1317.6 | 1311.1 | 1257.8 | 1254.3 | 1256.9 | 1247.8
M2 WtAvg+5°C (1236.6°C) | 1242.5 | 1239.6 | 1314 | 1307.5 | 1254.2 | 1250.7 | 1253.3 | 1244.2
M3 RT-Wtd+5°C (1235.5°C) | 1241.4 | 1238.5 | 1312.9 | 1306.4 | 1253.1 | 1249.6 | 1252.2 | 1243.1
Actual FCE Dropout | 1250 | 1250 | 1250 | 1250 | 1250 | 1250 | 1250 | 1250
Max Recipe Target | 1240.2 | 1240.2 | 1240.2 | 1240.2 | 1240.2 | 1240.2 | 1240.2 | 1240.2
Zone Setpoints (°C)
Zone | Type | M1 | M2 | M3
Z1 | Preheat | 1246 | 1243 | 1241
Z2 | Preheat | 1243 | 1240 | 1239
Z3 | Soaking | 1318 | 1314 | 1313
Z4 | Soaking | 1311 | 1308 | 1306
Z5 | Heating | 1258 | 1254 | 1253
Z6 | Heating | 1254 | 1251 | 1250
Z7 | Heating | 1257 | 1253 | 1252
Z8 | Equalising | 1248 | 1244 | 1243
FCE | Slab exit | 1250.0 | 1250.0 | 1250.0
NOTE ON Z8 vs FCE: Z8 setpoints (M1=1247.8°C, M2=1244.2°C, M3=1243.1°C) are all BELOW the actual FCE dropout (1250°C). This is CORRECT. The slab carries heat from soaking zones Z3/Z4 (which operate at 1317–1317°C) through the equalising zone. Z8 equalises top-bottom temperature difference — it does not need to be hotter than the slab surface. FCE dropout is the OUTPUT of all 8 zones working together, not just Z8.

## Slide 6
DECISION MATRIX — Which Model for Which Schedule
Based on real Hazira schedules and production conditions
1
% Slabs Below Recipe > 10%?
YES → USE M1
NO → Check next →
2
Recipe Spread > 18°C?
YES → USE M1
NO → Check next →
3
Residence Time Spread > 40 min?
YES → USE M3
NO → Check next →
4
New grade or API/quality-critical?
YES → USE M1
NO → Check next →
5
FCE routinely +12°C over recipe?
YES → USE M2
NO → USE M2 (default)
RESULTS
S19
M1
S15
M2
S14
M3
S18
M2
🌐 INTERACTIVE HTML PROTOTYPE — RHF_Setpoint_Optimizer.html
📋 Schedule Tab: Select any of the 4 real schedules → see grade mix, model setpoints, zone profile chart, and recommendation
🎛️ Simulator Tab: Drag sliders for each grade count → live model recalculation, zone chart, and auto-recommendation logic
📐 Model Logic Tab: Full explanation of M1/M2/M3 + corrected Z8 physics explanation + zone offset heatmap
🌡️ Zone Profile Tab: Select schedule + model overlay → zone temperature chart + complete setpoint table with Z8 vs FCE comparison